## Slide 1: ACE: the Atomic Cryptography Extension
Security Architect, CPU Team, Qualcomm
Roberto Avanzi with Ruud Derwig, Luis Fiolhais, Radim Krčmář
ravanzi@qti.qualcomm.com

## Slide 2: Important notice
This is neither the ACE recently announced by Intel and AMD
nor IBM’s Assured Confidential Execution for RISC-V.

## Slide 3: The Proposal

## Slide 4: Proposal
ACE defines an ISA extension for full-round cryptographic operations using Cryptographic Contexts, indivisible data structures {metadata, key(s)} that keep the key(s) hidden, and can be stored in architectural states called Cryptographic Registers.
Processes data one block at a time.
ACE uses Crypto Registers instead of the clear key.
The contents of the CRs are protected by the HW.
Metadata determines which algorithm can be used with the key.
Multiple CRs can be active at the same time. Encoded like registers (0..31). Fast switching!
The CRs are architectural (per hart, can be context switched — not global).
Interface can support several algorithms, no need for new instructions each time.
Notes: Protected by the HW = in internal memory, not accessible to SW.

## Slide 5: The Problem

## Slide 6: Use cases
Decryption of premium content (including local decryption of LLMs/SLMs).
Key management.
Communications.
Automotive (need for agile use of several keys at the same time, respect expected timing).
Storage encryption.
Cryptography for small embedded devices.
Secure boot and/or attestation in bootloaders without invoking a separate HW block.
Virtualization and Multiple Worlds (isolation of keys between environments).
Notes: More exotic applications such as Page-fault-driven page-based memory encryption in SW (SoftME, MemShield, …) can also be accelerated by this proposal.
(Nice to have: small and portable code base (reduce SW vulns), unified interface to key management.)

## Slide 7: Current solutions are inadequate
Because:
Round-based ISAs (AES instructions) need to add the key in clear between the rounds.
⇒ We need full-round instructions, so the key is a “hidden” input & cannot be recomputed.
Lack of trust, no key management (blocks) except in external IP blocks or TEE applets.
These require substantial work to configure shared mem buffers, copy data around.
In some modes, derived values should also not leak. [*]
⇒ We need to hide these derived values as well. Sometimes they are just added.
⇒ We need to support (some) modes, not just primitives.
⇒ Many modes have derived keys: supporting them reduce resource use.
Existing solution tend to trade performance against trust.
Notes: [*] such as AES-GCM-SIV (and future accordions), encryption and authentication keys,

## Slide 8: Current solutions are inadequate (for Risc-V)
Intel has Key Locker:
  Only fundamental primitive (AES 128/192/256), and direction seems to the one set of instructions PER primitive–does not scale (EU CRA ACM?)
  No support for modes of operation (some break if intermediate values leak)
  Very CISC-y (instructions are simple in the ISA–need tons of microcode)
IBM has the Protected Key feature:
  Does not scale like Intel’s
  Very CISC-y: Instructions take multiple pointers, all processing in memory, payloads processed in one go. (Completely microcoded.)
  Support for public key crypto, intermediate values exposed to memory

## Slide 9: The Solution

## Slide 10: Proposal
ACE defines an ISA extension for full-round cryptographic operations using Cryptographic Contexts, indivisible data structures {metadata, key(s)} that keep the key(s) hidden, and are stored in architectural states called Cryptographic Registers.
Processes data one block at a time.
ACE uses Crypto Registers instead of the clear key.
The contents of the CRs are protected by the HW.
Metadata determines which algorithm can be used with the key.
Multiple CRs can be active at the same time. Encoded like registers (0..31). Fast switching!
The CRs are architectural (per hart, can be context switched — not global). HOW?
Interface can support several algorithms, no need for new instructions each time.
Notes: Protected by the HW = in internal memory, not accessible to SW.

## Slide 11: Some necessary features
Cryptographic Contexts (CCs) in Crypto Registers (CRs):
How to initialize / save / restore them?
PROVISION reads metadata and secrets from memory, places them into a CR.
  This creates a Cryptographic Context, binding the key(s) to the metadata.
Then we can EXPORT (and IMPORT) a CC securely, using encryption and authentication.
  Exporting uses a Context Sealing Key (CSK, known only to Machine) …
  … and creates Sealed Cryptographic Contexts (SCC).
Export / Import is necessary for context switching ...
  … and to pass keys from one environment to another.
  Compatibility with sleep / hibernate and VM migration.
Notes: Dropbox: Once something is in, it is unretrievable by those that put it in, and only available to authorities. The ACE unit is the authority here.
Optional mutual isolation of keys between environments
⇒ CSK configurable (by Monitor/Machine).
This is also necessary to support VM migration to other devices.

## Slide 12: Life of a CC (example)
TEE, I need the key to decrypt the data I got!
OK!
I am on it!
CR
CR
SCC
SCC
User
TEE
BU METİNDEN TEK BİR KELİME BİLE ANLAMIYO-
-RUM.

## Slide 13: How the User decrypts stuff in ACE
I CAN NOW UNDERSTAND EVERY SINGLE WORD OF THIS TEXT.
BU METİNDEN TEK BİR KELİME BİLE ANLAMIYO-
-RUM.
CR
Single Block
of Ciphertext
Single Block
of Plaintext
ACE Execution Unit

## Slide 14: What — High Level View of the Solution
The most important (pseudo–)instructions are:
PROVISION Kn, %offset(Xs) | Loads { metadata, key(s) } from memory and places them in a CR;
CLEAR Kn | Erases/invalidates the content of a CR; (pseudo-insn using ace.setst)
EXPORT %offset (Xd), Ks | Encrypt +authenticates the contentsof a CR, stores it in memory as an SCC;
IMPORT Kd, %offset(Xs) | Authenticates, decrypts and loads an SCC back into the system.
ace.exec Vd, Kn, Vs | Performs a cryptographic operation on a block (e.g., 128 bits) of the input according to the algorithm configured in the CR and its current state.
ace.setst Kd, #imm | Determines whether we encrypt or decrypt, selects the stage of an algorithm, etc. prepares CRs for provisioning/import/export–or terminates the procedure. This is the most important insn for CR management.
The inputs/outputs of the ACE instructions are: Crypto Registers, Vector Registers, an internal buffer/closely coupled memory called the ACEIOBUF, and memory.
Notes: (*) Alternatives can be discussed: By using one bit in ace.exec to genote whether we are using GPRs or vector registers, we can instead use pairs of 64-bit GPRs or quartets of 32-bit GPRs. Since no other change would be needed in the entire architecture, we suspend further discussion on this until later :-) For 256-bit wide ciphers, we may need to group more GPRs, whereas the vector unit allows more easy “resizing”.
All formats are architected.

## Slide 15: Life of a CC (example)
Requester SW needs a CC to process some payload.
A Secure Completer sets up metadata (64-bit field with: Algorithm, Side-Channel Protection Level, Key Type, Access / Usage Policies) followed by the key(s) in memory at *X1.
Then, PROVISION K0,0(X1) configures CC K0 with the metadata and the keys.
Completer uses EXPORT 0(X2),K0 to write the SCC to memory (at, say, *X2, shared buffer).
The Requester can IMPORT it to the context number of choice.
Requester now can use ace.exec and ace.setst to perform cryptography!
A process can also configure CCs for itself to reduce exposure of keys in the memory, or to take advantage of performance, share code with libraries that also use CCs provisioned from outside…

## Slide 16: What we don’t (want to do)
Directly interfacing to external key providers secure SW/HW can do it and deliver keys to us.
Revocation. This is a deliberate Non-goal.
Notes:   reverse sandboxed environments = enclaves, realms, TZ, Secure Worlds/Secure Supervisor Domains

## Slide 17: Why revocation is a deliberate Non-goal (skip this slide first time)
It is a very complex feature.
  It may require unbounded structures
  Needs co-mgmt of secure memory with host stack.
Also, user SW in the use cases that require revocation use derived (session) keys.
  But, in these protocols only root keys get revoked
Need to check keys often.
  Overhead, and it may deteriorate over time.
So, revocation logic should stay in the same reverse sandboxed environments (enclaves, realms, TZ) used for key delivery, and out of the ACE unit itself.

## Slide 18: What we don’t (want to do): Algorithm-specific instructions
The way of bad ISAs:
Let us introduce a keybox and a one shot-AES instruction.
Let us add caching of keyboxes!
Let us add an AES-XEX instruction to avoid leaking the intermediate mask while computing AES-XTS and AES-OCB…
Let us add an SM4 instruction.
Let us add an SM4-XEX instruction.
In the EU, the CRA is going to introduce several approved algorithms.
…
Instead, in ACE the algorithm is expressed by the CC, and the algorithms are discoverable.
Notes: I was at ARM, where I learned to hate non-orthogonal things and gradual erosion of the encoding space.

## Slide 19: Metadata
The metadata in a CC
  Selects a specific algorithm, e.g. AES and some modes (ECB, XEX, GCM, GCM-SIV).
  Can limit a confidentiality algorithm to only encryption or decryption.
  Limits which process / EL / VM / Device / Boot Cycle can use the keys.
State embedded in CC (CR inside ACE unit; SCC in memory)
The rules of the architecture and of the algorithm in a CC
  Determine the current state and the states one can transition to.
  The semantics of the operations performed in any given state by ace.exec / ace.setst.
  Define Error States as well.

## Slide 20: Metadata
Name | Description
Algorithm AlgorithmPolicy | Algorithm and Allowed Variants
SCProtection | Side Channel Protection
State StateExtension | State of the State Machine
ConfigStatus | Is the CR fully provisioned or being provisioned / exported / imported ?
ImpDataLen | Length of an optional implementation dependent information block
UsagePolicy | Can M / HS / VS / U / Debug perform cryptography with this CR?
Locality | Restrictions
AlgorithmUse | Useable by the Algorithm (not the implementation)
ExpirationDate | Expiration Date

## Slide 21: Algorithms (choice)
We architect several algorithms, and also define a minimal subset–probably a subset of:
AES-128 and AES-256 encryption and decryption.
AES-CTR, AES-GCM, AES-GCM-SIV, AES-XTS, AES-CMAC using AES-128/256.
SHA-2, SHA-2-HMAC.
Also, all (most?) elliptic curves in use. We will define PQ soon.
The list of other architected algorithms is TBD, but it should include at least
AES-192, alone and with the above modes.
SM4 Block Cipher.
The Ascon suite (Ascon-128/128a-AEAD, Ascon-Hash, Ascon-XOF, Ascon-80pq).
SHA-3, SHA-3-HMAC.
SM3 Secure Hash.
The list can be extended by the architecture owner + space for custom algorithms.

## Slide 22: Issues
The functionality can be expressed as single but VERY complex instructions.
  This would not by Risc-V-y.
  Must split certain functionality into more instructions, each as simple as possible.
This is a security feature–any place where we can break/interrupt/preempt its operations is an attack surface. We need to expose state, but we cannot expose exploitable state.
Manage variable length inputs and outputs
  Loads/Stores longer than XLEN can be done by each implementation in the order they want. This is also potentially annoying for security.
Support cores with V and without.
Need to be able to support multiple nested interruptions/exceptions/preemptions and export/re-import partially configured states. All without breaking security/allowing corruption/forgery.
Support migration.
It is like juggling with 14 balls (2017 world record by Alex Barron with 14 beanbags).
Overall architecture complexity higher than RVV.

## Slide 23: The Model
The ACE Unit works like an attached unit.
Similar to streaming accelerators (Arm SSVE/SME, or RISC-V’s AME). (Doesn’t have to be implemented as one.)
Can have its own LSU.
Can work asynchronously from other cores.
Can be shared amongst multiple cores.
Keeps an architectural state per hart (hardware thread).

## Slide 24: A possible implementation
Core/Hart
Core/Hart
architectural state
architectural state
Additional
State (if needed by implementation)
“Decoder”
Crack + queue operations
P
I
P
E
P
I
P
E
P
I
P
E
Write outputs
Fetch inputs
ACE XU
Notes: Aechitectural state = all registers, including the CC memory.

## Slide 25: Example 1: Simple Decryption, no Authentication
Process calls OS API to get an AES-decrypt SCC from a key mgmt applet or HW block. Pointer in X5.
Allocate memory for plaintext buffer.
IMPORT K0, (X5) // Import the SCC into CR K0
ace.getmd X1, K0 // Gets error state
if error state in X1 then this means that encryption was not allowed: handle error.
ace.setst K0, #ace_state_decrypt // Not mentioned before, necessary if CC allows enc & dec.
ace.getmd X1, K0 // Also gets errors
if error state in X1 then this means that encryption was not allowed: handle error.
for i = 0 to ceil(len_in_bytes(plaintext)/16)-1 do
  load V0 from *(ciphertext+16*i)
  ace.exec V0, K0, V0 // Decrypt one block of the ciphertext
  store V0 at plaintext+16* // Write to plaintext buffer
ace.setst K0, #ace_state_initial // Ready to do more! (Actually, superfluous for ECB…)
Important
If the package is an SM4-encrypted buffer, and the CC is configured with SM4, the same binary works!
Notes: Since we are using AES, i.e. 128-bit blocks, we need to operate over a vector of 4 32-bit elements: in some archs like Risc-V this requires an extra operation such as
vsetvli zero, 4, e32, m1, ta, ma
We shall add also code snippets for the transition
User's "world" -> MM -> applet's world -> applet -> MM -> User's "world" - > user process
Ruud: Why is import/export working directly on memory, whereas exec operates on vector registers? Seems inconsistent. This can be solved in various ways: having a version that uses GPRs or a subset of RVV.
Regarding ace.setst, this can also be implemented either as a CSR write or an an instruction that ALSO performs a CSR write, like the Vector setup instructions (so we also have a precedent for such an approach).

## Slide 26: How to estimate necessary CRF capacity
AES-256 XTS state:
  512 bits of keys + 64 bits MD + 128 = 704
  704 * 32 = ~ 22K bits
This is too big, what if we target AES-128 and allow for some “big ones”?
  (64+128) * 32 ~ 6K bits
  If capacity exhausted, ace.prov / IMPORT will say NO / raise exception
  SW will offload some of the others
To determine the actual parameters: talk to SW guys, analyze some SW.

## Slide 27: Why we need this proposal

## Slide 28: Why we need to submit the proposal
Useful and scalable feature — single interface instead of new instructions for each algorithm
It supports modes, and can work as an interface
  public key algorithms,
  complex and large functions (Keccak, post-quantum PK algorithms) as well,
  side-channel hardened versions of all the above.
Makes SW simple, portable, reduces bugs, saves dev time and cost.
Frees small cores from having to handle the modes themselves in SW.
It is very actively being worked in RVI’s “High Assurance Cryptography” TG.
If implemented as an attached unit, it can even work in heterogeneous clusters (imagine having some ARM cores, some RISC-V microcontrollers, and maybe a few Hexagons). Also shifts optimizations to the ACE unit, keeping small cores clean.
Notes: The first three reasons should also persuade the 3 letter entity.

## Slide 29: State of the Specification

## Slide 30: State of the Specification
≥ v0.5.0, quite mature:
  Feature complete.
    Instruction behavior described in detail.
    Almost all algorithms fully specified.
    Versions with vectors and without.
  Error handling, exception handling, interrupt / resume.
  Pseudocode examples to explain usage.
  While we have defined Risc-V (Risc-V-y!) instructions, we want data formats used on other ISAs for interoperability. Who shall maintain data formats and algorithms?
The latest release of the spec can be downloaded from at:
https://github.com/riscv/riscv-high-assurance-cryptography/releases
Notes: Algorithms specified : data structures, state machine, error handling.
ARM version would have a subset of features: some resumable instructions would be restartable only. Simpler Worlds model.

## Slide 31: Instructions and Metadata in Brief

## Slide 32: Provisioning / Export / Import (as of today)
Removing error handling, Provisioning is performed by the following steps:
  ld loads (64 bits of the) metadata from memory
  ace.setst prepares a CR to be provisioned, pass the metadata as parameter, check its validity, store it in the CR.
  ace.load loads the rest of the provisioning information into the CR.
  ace.setst makes the CR available to software.
Exporting a CR as an SCC consists of the following steps:
  ace.getmd exports the metadata from the CR to be able to determine its size and allocate resources.
  sd store metadata
  ace.setst prepares a CR to produce a SCC, includes encrypting its contents and computing the authentication tag(s).
  ace.store stores the rest of the SCC to memory.
  ace.setst internally restores the CR in a form available to software.
Importing a SCC into a CR is similar to provisioning:
  ld loads (64 bits of the) metadata from memory
  ace.setst prepares a CR for importing a SCC, pass the metadata as parameter, check its validity, store it in the CR.
  ace.load loads the rest of the SCC information into the CR.
  ace.setst authenticates and decrypt the SCC and make the CR available to software.

## Slide 33: Provisioning Code
ld t1, 0(t6) # load MDH bits [63:0] from memory
li t3, #23
restart:
ace.setst K(t0), t1, #provision_open # open CR for provisioning, load MDH[63:0] in it
ace.getst t2, K(t0) # get _State_ field from MDH[63:0]
bltu t3, t2, handle_errors # errors (larger than 23, i.e. ≥ 24)
beqz t2, handle_errors # handle error (is _Off_ needed?)
ace.load K(t0), 8(t6) # load rest of PI starting with MDH[127:64]
ace.getst t2, K(t0) # get _State_ field from MDH[63:0]
li t3, #ace_state_off # compare to off state
beq t2, t3, restart # CR cleared means force restart
ace.setst K(t0), #provision_close # possibly reconstructs data
ace.getst t2, K(t0) # get _State_ field from MDH[63:0]
bltu t3, t2, handle_errors # handle other errors (> 23, i.e. ≥ 24)
success:

## Slide 34: Export Code
ace.size t2, K(t0) # get size of the data to export
{...} # here goes the code that allocates the buffer to store the exported data
ace.getmd t1, K(t0)
If ConfigStatus field in the metadata = CfgStcomplete, the following ace.setst prepares the serialized, encrypted and authenticated internal representation of the CR for export, computes the SIV(s), then change ConfigStatus to CfgStExporting. Otherwise, it does nothing.
ace.setst K(t0), export_open
sd 0(t6), t1 # Export original _ConfigStatus_ to memory
The next instruction stores all data starting with the 8th byte of the MDH. In case of interrupt/exception, the handler will decide whether to keep acestart or clear it to force restart. The instruction gets the length of the blob to export from the MDH no special handling from the SW is necessary.
ace.store 8(t6), K(t0)
success:
Reset MDH[63:0] to the previously saved value. If the saved ConfigStatus is CfgStcomplete, the operation also re-decrypts the state and makes the CR available to software, otherwise it does nothing and leaves the CR state in the serialized and encrypted format.
ace.setst K(t0), t1, export_close

## Slide 35: Import Code
ld t1, 0(t6) # load MDH bits [63:0] from memory
li t3, #23
restart:
ace.setst K(t0), t1, #import_open # prepare CR for import, load MDH[63:0] in it
ace.getst t2, K(t0) # get _State_ field from CR (after checks!)
bltu t3, t2, handle_errors # errors (larger than 23, i.e., ≥ 24)
ace.load K(t0), 8(t6) # load all the rest starting with MDH[127:64]
ace.getst t2, K(t0) # get _State_ field from MDH[63:0]
li t3, #ace_state_off # compare to off state
beq t2, t3, restart # CR cleared means force restart
ace.setst K(t0), #import_close # decrypt/authenticate CR, possibly complete it
ace.getst t2, K(t0) # get _State_ field from MDH[63:0]
bz t2, handle_errors # handle _Off_ state (needed ? double check)
bltu t3, t2, handle_errors # handle other errors (> 23, i.e., ≥ 24)
success: